## Slide 1: Major Changes
Adding an initial planning step to algorithm
  Use RRT* to plan a core path from the starting location to the goal location
  Take returned path to setup sampling bounding boxes
  Since the path reaches the goal position, we need only to make sure samples can touch the core path
  Now select samples via sequential greedy method
Plan a path for all agents through selected samples using DMA-RRT* algorithm
  Ensures collision avoidance between agents and obstacles

## Slide 2: Safe Path Planner
Given:
  Obstacle Coords
  Starting and goal positions (for all agents)
start
goal

## Slide 3: Safe Path Planner
Given:
  Obstacle Coords
  Starting and goal positions (for all agents)
  Some interval at which the interaction constraint is considered (total number of time slices to generate)
start
goal
Time slice bounding sets

## Slide 4: Safe Path Planner
Given:
  Obstacle Coords
  Starting and goal positions (for all agents)
  Some interval at which the interaction constraint is considered (total number of time slices to generate)
Local planner for viability test
(relatively quick, small price to pay
in obstacle “shadowing”)
After samples are generated and selected, run DMA-RRT*

## Slide 5: DMA-RRT*
Now we can bolt-on a multi-agent path planner that considers
  Obstacles
  Agent-to-agent collisions
  Decentralized processing
Build in pauses at selected samples to make sure agents can interact as planned
start
goal
Time slice selected to enforce interaction (can be swapped out with a connected graph constraint as opposed to complete

## Slide 6: Result
DMA-RRT* results with randomized obstacles and 2 agents
Color along path is encoding time, used for collision avoidance visualization
“sidestep” to avoid the other agent
Sub-goal position

## Slide 7: Sampling Scheme
Starts at mean start position of all agents, and goes to mean goal position of all agents
Samples are blocked by obstacles, as expected
Note sampling locations are not centered around waypoints, but rather at regular distance-based intervals
Obstacle shadowing, samples require clear view to center of bounding set

## Slide 8: With Greedy Selection Scheme
Now we use the greedy sample selection scheme that the paper is actually about
Selected samples are shown in green

## Slide 9: More test cases
Example of why we need to wait at interaction locations
“jags” away to make space to be within collision radius at interaction point
Agents’ collision radius is actually larger than the interaction radius here, and since the waiting at TOIs has yet to be implemented, agents are not actually able to be at correct locations at correct times